## Slide 1: Australian Calibration And Validation Activities
Cindy Ong
CSIRO

## Slide 2: Summary of Australian Calibration And Validation Activities
  Recent discussion paper: Malthus, T., Ong, C., Thankappan, M. & Grant, I. (2016). Sustainability Of Critical Calibration Facilities To Support Earth Observations From Space;
  10 calibration facilities;
  Activities range from optical, SAR, satellite altimetry;
  Main organisation CSIRO, together with GA, BoM, UniTAS, Curtin Uni, Monash University and UoW;

## Slide 3: Aim
To build a vicarious calibration site specifically for imaging spectroscopy missions underpinned by instrumentations and laboratory calibration facilities at least meeting (and aiming for beyond) those of current CEOS endorsed vicarious calibration sites.

## Slide 4
Future spaceborne imaging spectroscopy EO missions – launch and life time
ESA
28 29 30
EnMAP
PRISMA
HISUI
GISAT
FLORIS / FLEX
Sentinel-2B
Shalom
CCRSS
Resurs-P No.4
Resurs-P No.5
ECOSTRESS
Boeing?
CartoSat-3
HYPXIM-P
2000 01 02
University of Hawaii, USA
Roscosmos, Russia
HyspIRI
Sentinel-2A
… 14 15 16 17 18 19 20
HiakaSat
Resurs-P No.3
21 22 23 24
25 26 27
China Commercial, China
Roscosmos, Russia
ASI, Italy
ISRO, India
Roscosmos, Russia
JPL, USA
Boeing, USA
ISRO, India
DLR, Germany
METI/JAXA, Japan HISUI:METI/ISS: JAXA
ASI, Italy/ISA, Israel
ESA, UK
CNES, France
NASA/JPL, USA
DLR, Germany / Teledyne, USA
DESIS/TAIS

## Slide 5
Systematic Search For Vicarious Calibration Site Using Landsat TM Archive
Green vectors show high rainfall zone >600 mm pa
Red circles show radius of 400 km (half day’s drive) from major airport
Image is VNIR-SWIR temporal means
Lake Lefroy
Strzelecki Desert
Shark Bay

## Slide 6
Central Desert Temporal Means And Coefficient Of Variations (VNIR-SWIR)
Means
Coefficient of variation

## Slide 7: Spatial, Temporal Variation
VNIR-SWIR temporal means
VNIR temporal variation
SWIR temporal variation

## Slide 8: Compositional Variation
ASTER silica
ASTER ferric
oxide
ASTER AlOH
ASTER MgOH

## Slide 9
Central Desert Logistics
Access
  ~ 700 km N of Adelaide
  Sealed roads from Adelaide to Lyndhurst (~600km N), good unsealed road to Marree (~80km N), good unsealed road to Muloorina Station (~80km N), unsealed tracked to site (~ 50-80km E).
  Nearest airport Olympic Dam, ~ 150 km away;
  Nearest town and accommodation Maree, ~ 100 km away;
  Nearest accommodation Muloorina Station, ~50 km but now mainly used by BHPBilliton;
  Supplies including drinking water and food best obtained from Adelaide;

## Slide 10
Central Desert Logistics
Landforms
  Lake Eyre covers 144kmX77km, 15.2 metres below sea level, it is the lowest point in Australia. Flood waters cover lake once every 8 years on average, filled to capacity 3X in the last 160 years;
  Surrounding area covered by red sand dunes and mesas, rising from salty claypans and stone-strewn (coarse gibber) tablelands;
Vegetation
  Vegetation is generally sparse. Canegrass and scattered clumps of mulga and acacias grow on the red sand dunes and the occasional stand of acacia can be seen on the coarse gibber tablelands. Nitre-bush, samphire, needlebush and native willow are also found in the Lake Eyre area.
  Other areas are grazed and there are an abundance of cattle in some parts of the landscape. NB. Risk of animals for instruments
Central Desert Logistics

## Slide 11
Central Desert Logistics
Communications
  No communication except for satellite even at Marree which had broad band reduced;
  Satellite phone essential;
Permissions
  Large areas which are sand plains are now on BHPBilliton lease area behind gated compounds, permissions required from BHPBilliton. Keys available from Moorlina Station owners but permissions needed prior to this;
  Other areas require permissions from land managers which are either pastoralists or government land managers as the area is with the Kati Thanda-Lake Eyre National Park;
  Aboriginal heritage permissions will most likely also be required to install instruments if on nature reserve;

## Slide 12
Climate Data From Lake Eyre (Weather Station In Middle Of Central Desert)

## Slide 13: Lessons Learnt
The use of long term archive data provides a good start but no current sensor can detect dry vegetation prevalent in arid climate => justification for imaging spectroscopy;
No matter how good a site looks on desktop study, field campaign extremely important to check out all logistics;
Site access and communication extremely important => no one should die going to site, instruments need servicing and data needs to be retrieved autonomously;
Fit for purpose: Central Desert may be useful as PICS. There is already a CIMEL there;

## Slide 14: Pinnacles Desert Location And Logistics
Access
  Lat Lon: 30°35'24.67"S, 115° 9'23.84"E, elevation 30-70 m
  ~ 250 km N of Perth
  Nearest airport Perth
  Nearest town and accommodation Cervantes, ~20 km away
  Sealed roads all the way from Perth to Nambung National Park
  ~ 1 km walk into sand dunes
Landform
    Undulating sand dunes (2x5 km) consisting dominantly of quartz, carbonate, kaolinite, and minor amounts of iron oxide
  Vegetation
    Low dry heathlands, 170 angiosperms: eg. coastal wattle, sea nymph, acorn banksia, cowslip orchid, ringed wallaby grass and coast hop-bush. 1 gymnosperm: swamp cypress

## Slide 15: Pinnacles Desert Logistics
Communications
  3 / 4 G
  Satellite
  Landline
Permissions
  Department of Parks and Wildlife
  Aboriginal Heritage
  Need to minimise disturbance especially if on dunes
  Bitumised, locked up areas around the Discovery Centre
Security
  Dunes are in Nambung National Park
  Dunes are at least 1 km from tourist traffic area, no tracks except for animals (Emu and Kangaroos) in 7 visits
  Park is manned by rangers

## Slide 16: Pinnacles Desert Climate Data From Nearest Weather Station

## Slide 17: Spatial, Temporal Variation
10 year Temporal Means VNIR-SWIR
10 year Temporal Means VNIR
10 year Temporal Means SWIR
Coefficient Of Variation VNIR-SWIR

## Slide 18: Compositional Variation
MgOH (Carbonate) Abundances
AlOH (Clay) Abundances
Silica (Sand) Abundances
DEM

## Slide 19: Work Planned For The Near Future
Permissions For Instrument Installation Submitted
  Pending information on structure and specifications on radiometric instrument;
Instrumentation Obtained And Planned For Installation
  CIMEL (on Aeronet);
  Weather station linked to CIMEL;
  COSMIC Ray Probe (on national and international network);
Instrumentation Aspiration
  Automated acquisition of complete VNIR-SWIR spectral measurements feeding into systems such as RadCalNet and/or receiving/processing hubs;

## Slide 20: Work Planned For The Near Future
Evaluation of surface composition
  WV3 data scheduled for fine scale compositional assessment and DEM
  Hyperion scheduled for spectral characteristic
  All scheduled data will be used for decision on final area selection
  Laboratory characterisation of samples (VNIR-SWIR, TIR, XRD, LOI?)
  Field campaign for site characterisation, sample collection, field spectral measurements (VNIR-SWIR and TIR (TBD));
  Laboratory characterisation of samples (XRD, size fractions, etc.);
  Investigate satellite BRDF characterisation;
  Hyperspectral and high spatial resolution temporal characterisation of selected site where possible;
  Field BRDF characterisation (DSTO, UCL);