## Slide 1: Optical Mission Status

## Slide 2: Outline
Sentinel-3 mission overview
Overview of optical instrument commissioning activities
OLCI performance
SLSTR performance
Conclusion

## Slide 3: Sentinel-3: launch
Launched on a Rockot from Plesetsk, Russia, at 17:57 GMT on 16 February 2016
Notes: POD: This is Precise Orbit Determination and includes the on-board GPS units, the Laser Retroreflector and the CNES DORIS system.

## Slide 4: Sentinel-3: mission
Sentinel-3 A is the first of a series of 4 satellites ensuring 20 years of operational ocean and land monitoring
Developed by ESA for the European Commission and co-operated by ESA/EUMETSAT
The spacecrafts carry four main instruments:
  OLCI: Ocean and Land Colour Instrument
  SLSTR: Sea and Land Surface Temperature Instrument
  SRAL: SAR Radar Altimeter
  MWR: Microwave Radiometer.
These are complemented by three instruments for Precise Orbit Determination (POD):
  DORIS: a Doppler Orbit Radio positioning system
  GNSS: a GPS receiver, providing precise orbit determination and tracking multiple satellites simultaneously
  LRR: to accurately locate the satellite in orbit using a Laser Retro-Reflector system.
Notes: POD: This is Precise Orbit Determination and includes the on-board GPS units, the Laser Retroreflector and the CNES DORIS system.

## Slide 5: Instrument Swath and Satellite Orbit
Orbit type
Repeat cycle
LTDN
Average altitude
Inclination
Repeating frozen SSO
27 days (14 + 7/27 orbits/day)
10:00
815 km
98.65 deg
1400 km SLSTR (nadir)
740 km SLSTR (oblique)
1270 km OLCI
SRAL (>2 km) and MWR (20 km) nadir track
Instrument Swath Patterns
Notes: Sun-synchronous frozen orbit close to 800 km
• Required for optical observations continuity
• Topography mission requirements
• Repeat cycle > 20 days,
• Optimum Topography mission spatial sampling
• Minimization of aliasing
• Ocean Colour mission requirements
• 2-day global coverage with 2 satellites, 4 days with one
  Implies a sub-cycle of 4 days
• Local time of observation shall be > 10 h to avoid morning haze
• Sea Surface Temperature mission requirements
• Local time at node shall be < 11 h to avoid skin effects
The second S3 satellite shall be positioned ensuring the best compromise between:
  The minimum OC mission Revisit Time (the most stringent RT requirement due to Sun-glint constraint)
  The most regular Topography mission spatial sampling (smallest 27-days mesh cell size)
Phasing the two satellites on the same orbit with an anomaly difference of 180° fulfils both objectives.

## Slide 6: Preliminary performance assessment

## Slide 7: Optical calval activities
Sentinel-3 Phase E1 Optical calval activities were conducted under the ESTEC Sentinel-3 Project responsibility between launch and end of commissioning phase (12 July 2016) => 5 months
Optical calval activities relied on key industrial partners
ESTEC strongly supported by:
  ESOC
  ESRIN
  EUMETSAT

## Slide 8: OLCI instrument

## Slide 9: First OLCI Images from Sentinel-3
Sunrise over Svalbard,
14:09 GMT on 29 February 2016
Notes: 21 Bands, 1270 km swath, 300 m resolution

## Slide 10: OLCI vs. MERIS
  Compared to MERIS:
  100% overlap with SLSTR
  More spectral bands (from 15 to 21): 400-1020 nm
  Wider swath: 1270 km
  Full res. 300m acquired systematically for land & ocean
  Improved characterization, e.g. straylight, camera boundary characterization
  Reduced sun glint by camera tilt in west (12.6°)
MERIS Bands | λ center | Width
Yellow substance/detrital pigments | 412.5 | 10
Chl. Abs. Max | 442.5 | 10
Chl & other pigments | 490 | 10
Susp. Sediments, red tide | 510 | 10
Chl. Abs. Min | 560 | 10
Suspended sediment | 620 | 10
Chl. Abs, Chl. fluorescence | 665 | 10
Chl. fluorescence peak | 681.25 | 7.5
Chl. fluorescence ref., Atm. Corr. | 708.75 | 10
Vegetation, clouds | 753.75 | 7.5
O2 R-branch abs. | 761.25 | 2.5
O2 P-branch abs. | 778.75 | 15
Atm corr | 865 | 20
Vegetation, H2O vap. Ref. | 885 | 10
H2O vap., Land | 900 | 10
New OLCI bands | λ center | Width
Aerosol, in-water property | 400 | 15
Fluorescence retrieval | 673.75 | 7.5
Atmospheric parameter | 764.375 | 3.75
Cloud top pressure | 767.5 | 2.5
Atmos./aerosol correction | 940 | 20
Atmos./aerosol correction | 1020 | 40

## Slide 11: OLCI vs. MERIS
OLCI (2016/03/02 05:13 GMT)
Nadir
MERIS
MERIS (2006/03/02 @ 05:06 GMT)
Nadir

## Slide 12: OLCI vs. MERIS
The 1020nm band is suitable for improved atmospheric correction, to allow better water leaving reflectance retrieval in coastal regions.

## Slide 13: S3 OLCI: Technical details
Basic configuration similar to MERIS:
5 Camera Optical Sub Assemblies (COSA),
5 Focal Plane Assemblies (FPA),
5 Video Acquisition Modules (VAM),
1 Scrambling Window Assembly (SWA),
1 OLCI Electronic Unit (OEU) managing all the instrument functions,
1 calibration assembly allowing radiometric and spectral calibration.

## Slide 15: OLCI Performance
Overview
  Functional verification
  Radiometric Calibration
  Spectral Calibration

## Slide 16: Functional verification
The functional behaviour is as expected:
  Measurements are performed nominally with no gaps over the daytime of the orbit
  The on-board calibration are performed nominally outside the daytime part of the orbit Satellite Payload and house keeping data produced on board transmitted to ground without loss
  Temperature stability of the CCD and the Optical bench from which the instrument performances strongly depend on are well within specification.
  All observation modes / calibration sequences have been exercised
=> Fully functional

## Slide 17: OLCI spectral/radiometric calibration
OLCI is a self-calibrating instrument using on-board diffusers:
Every ~2 weeks routine with 1st white diffuser
Every ~3 months with 2nd white diffuser for ageing
Spectral calibration: Erbium Doped Diffuser (for spectral calibration)

## Slide 18: Radiometric gain variation from white diffuser – Mean across track gains (ACRI – L. Bourg)
Calibration gains show time variability believed to be related to:
  Star tracker anomaly => pointing model
  Uncertainties of diffuser BRDF model (already known from on-ground)
Stability improves with time.

## Slide 19: Independent radiometric assessment
CNES (SADE/MUSCLE) and ESTEC (DIMITRI) used for independent assessment:
Consistent results making use of different methods / implementations
Spectral consistency
OLCI radiances might slightly higher than expected but more data over longer period of time is needed to confirm and monitor the evolution
CNES (B. Fougnie)
ESTEC (M. Bouvet)
Notes: Put MERIS here

## Slide 20: Signal-to-Noise Ratio (SNR)
SNR performance are scaled down from Lcal to typical water radiance (Lref) with 2 different methods.
Results compliant, downscaling to be confirmed by ongoing analysis of EO images
ESTEC (J.-L. Bezy)
ACRI (L. Bourg)
Notes: Radiometric performance measurements (e.g., signal-to-noise ratios (SNR), non-linearity (NL)) demonstrate good performance for all cameras of OLCI-A,
The SNR test campaign demonstrated an excellent consistency of intra-camera (different spectral bands, spectra or full and reduced resolution modes), and inter-camera measurements. Also a good correlation between the test results and the SNR model was established. values for SNR, Noise equivalent Delta Radiance and the related TOA spectral radiance (L) are shown
Main Message:
Fully Compliant for all bands OA1 and OA2 marginal (SRD Req 2200, 2060 SNR)

## Slide 21: Radiometric: conclusion
On-board radiometric calibration functional
Dark signals are very stable and comparable to pre-flight characterisation (not shown here)
Periodic noise (noise affecting dark signals) analyzed in-flight and workaround proposed to reduce a non-compliance on absolute calibration accuracy for 940 and 1020 nm band at lowest level of the specified dynamic range (not shown here)
SNR is compliant with specification
Calibration gains show time variability
  Partly related to star tracker anomaly
  Uncertainties of BRDF model (already known from on-ground)
  Stability seems to improve with time
Vicarious calibration shows spectrally/spatially/dynamically/X-track consistent results, however a ~+3% bias.
  Actions are in place to further investigate this point (e.g., periodic noise correction in ground processing, yaw maneuvers to characterize BRDF diffuser in flight and perform calibrations at fixed geometry) during next phase.

## Slide 22: OLCI spectral programming
OLCI 21 bands
OLCI is programmable and can be configured to observe with highest spectral resolution, i.e., 46 single bands (µ-bands) instead of 21 nominal bands.
BC

## Slide 23: OLCI in-flight spectral calibration
spectral calibration is established using:
The on-board Erbium Doped Diffuser,
Fraunhofer Lines (for validation),
Oxygen O2A (for validation).
doping material Erbium absorption spectrum
Acquisitions scenario:
Orbit n = Diffuser-1 Cal (Band setting j)
Orbit n+1 = Diffuser-Er (Band setting j)
“Pink” Diffuser
Measurements
̶ 01/03
̶ 18/04
̶ 31/05
̶ Ground
ACRI – L .Bourg
03012016
04152016
Preflight
nominal
White Diffuser
Measurements
Fraunhofer lines on non-doped diffuser
Brockmann Consult – R. Preusker
Measurements over Natural target
OLCI was programmed in a way to observe the O2A absorption features over bright Earth targets
O2A spectrum
BC

## Slide 24: In flight spectral calibration results
Pre-flight characterisation confirmed in-flight (<0.15nm)
Small temporal trends since beginning of the mission (comparable to MERIS)
Spectrally fully compliant
Brockmann Consult – R. Preusker

## Slide 25: In flight geometric calibration results
After early mission pointing issues were fixed (e.g.: star tracker software), OLCI spatial feature matching with a Landsat reference imagettes database led to a first geometric calibration resulting into approximately sub-pixel accuracies. More data needed to fit a thermo-elastic model (seasonal variations) and further improve the calibration.

## Slide 26: SLSTR instrument

## Slide 27: ATSR Series
1991-2000 ATSR-1
1995-2008 ATSR-2
2002-2012- AATSR

## Slide 28: ATSR Series
2016 – Sentinel 3A

## Slide 29: the (A)ATSR series
Notes: Oceans are major Heat Reservoir
small changes in Ocean Temperature often led to large changers in Atmospheric Heating.

## Slide 30: S3 SLSTR: Scanning overview
The dual scan is based on two flat rotating mirrors and one flip mirror - switching between one view and the other
Each scan measures 2 Earth scan lines (multiple element detector arrays)
The scan mirrors rotate on a 300 msec time basis, ~half period of AATSR
The in flight calibration period is 600 msec
Each calibration source is seen by each view once every second scan cycle
Notes: The dual scan is based on two flat rotating mirrors and one flip mirror switching from one view to the other
The scan mirrors rotate on a 300 msec time basis, half of AATSR
The in flight calibration period is 600 msec, since each calibration source is seen by each view once every second scan cycle
Each view uses its own scanner (flat scan mirrors)
Each scan includes 2 IFOV earth views, calibration sources (BBs, VISCAL)
Views are seen by the front collecting and refocusing optics (Primary Mirrors)
Recombination optics to bring 2 optical paths into a single set of Focal Plane assemblies (FPA) after a common field plane used as intermediate field stop

## Slide 31: SLSTR First Image
Sentinel-3 SLSTR First Image over Egypt 03/03/2016
+
Last AATSR image over Egypt 07/04/2012
Google
Image
RAL

## Slide 32
AATSR 1km Spatial Resolution
SLSTR 0.5km Spatial Resolution (VIS channels) in 2106
Google
Image
S1 S2
S3
Large irrigation fields in the desert
(healthy vegetation appears in red)

## Slide 33: SLSTR IR channels switch on 23-Mar-2016
Sentinel-3 SLSTR First IR Image over Europe/North Africa
SLSTR L1b RGB from S1/S2/S3

## Slide 34: SLSTR IR channels switch on 23-Mar-2016
Large Sahara Dust Storm entering the Adriatic Sea resulting in about 50C temperature differences in BT
SLSTR L1b RGB from S1/S2/S3
SLSTR L1b S8
Dust Storm
EUM

## Slide 35: SLSTR Performance
Overview
  Functional verification
  VIS-SWIR Radiometric Calibration
  TIR performance

## Slide 36: SLSTR - Functional verification

## Slide 37: SLSTR functional and performance test summary
Test | Status
CPE functional test | PASSED
HK thermistors functional test | PASSED
Survival heater functional test | PASSED
Operational heaters functional test (incl. stability) | PASSED
Black Bodies heaters functional test (incl. stability) | PASSED
CCS functional tests (in launch lock, decontamination, cooling modes) | PASSED
FEE (incl. detectors) functional and performance test | PASSED
SUE functional and performance test (incl. stability) | PASSED
BBEU/TAEO functional and performance test | PASSED
Power consumption test | PASSED
ALL SUBSYSTEMS OPERATING NOMINALLY

## Slide 38: SLSTR - Instrument performance

## Slide 39: VIS-SWIR radiometric monitoring based on VISCAL (RAL – D. Smith)
VISCAL (white diffuser) is illuminated once per orbit
Oscillations in VIS channels caused by build up of water ice on VIS relay optics
Same behaviour as seen on ATSR-2, AATSR
VISCAL measurements are used to account for the long term instrument sensitivity changes (and short term changes due to the water ice contamination)

## Slide 40: Radiometric calibration
Vicarious methodologies using stable reference sites (SADE, DIMITRI) revealed a very good spectral consistency in the VIS and a possible ~+3% bias (wrt MERIS/MODIS-A) in the VIS
Radiometric issue in the SWIR (~-10 % at 1.6 μm and ~-40% at 2.2 μm). The issue at 2.2 μm was identified in the pre-flight calibration and thus confirmed in-flight by CNES/MUSCLE and ESTEC/DIMITRI => It was decided at the end of commissioning to revert to a calibration based on component level measurements (Diffuser BRDF, Mirror reflectances, UV window transmission, geometric factors) to derive the radiometric model before releasing the L1 data to the public and to continue investigations.
CNES (B. Fougnie)
ESTEC (M. Bouvet)

## Slide 41: VIS – SNR (RAL – D. Smith)
SNR evaluated from VISCAL peak signal
  Correspond to signals at ~20% reflectance
Values consistent with pre-launch results.

## Slide 42: SWIR – SNR (RAL – D. Smith)
SNR evaluated from VISCAL peak signal
  Correspond to signals at ~20% reflectance
Values consistent with pre-launch results.

## Slide 43: VIS/SWIR Conclusions
SNR requirement met
Dark Signals requirement met
Dynamic Range requirement met
Radiometric calibration will require longer period monitoring
Geometric calibration is ongoing with the prospect of delivering sub-pixel accuracy (not shown here) to first public users. Long term monitoring needed to derive thermo-elastic model.

## Slide 44: TIR radiometric calibration (RAL – D. Smith)
TIR calibration is based on 2 black bodies (‘cold’ and ‘warm’ to cover dynamic range)
Both black bodies temperature show good orbital stability< 0.1K
Gradients on black body plates in nominal configuration are stable.

## Slide 45: TIR Performance – Radiometric Noise (RAL – D. Smith)
NEDT values agree with pre-launch calibration and are well within specification,
Good initial long term stability,
No effects on performance due to the build up of water ice have been observed.

## Slide 46: Simultaneous Nadir Observation (SNO) with IASI (Eumetsat – I. Tomazic )
Initial results suggest very good correspondence with IASI-A.
SNO with IASI suggests that an anticipated stray-light bias in cold region (<220 K) seems to be lower than expected (~0.2 K) compared with 0.4K @ 220K from RAL measurements.
Validation activities to be continued.

## Slide 47: TIR Conclusions
Radiometric Noise
  NEDTs agree with pre-launch data and within specification
Radiometric Gains and Offsets
  Black body signals provide ‘continuous’ measurement of dark signals and the instrument is within specification
  Show good orbital stability
Black Body Calibration System fully functional
  Absolute accuracy:
    Difference in measured counts between the two black bodies during cross over test suggest calibration accuracy < 0.2K => compliance. Seems confirmed by IASI SNOs.
    Actions in place to further test and validate the radiometric model (internal straylight correction)

## Slide 48: Conclusions
Fully functional platform and optical instruments
Performance assessment carried out during the commissioning phase reveals instruments performing within specification with no major non-compliance => the commissioning phase was declared successful
OLCI: absolute radiometric accuracy and interband requirements remain under assessment until periodic noise corrections/yaw manoeuvres are implemented/carried out.
SLSTR: L1 processing will be updated (end July) to update pre-flight calibration coefficients and future corrections from vicarious calibration coefficients might be implemented (if still needed).
Feedback from the Sentinel-3 Validation Team and Expert Users (ESRIN- End June 2016) following pre-release of L1 and L2 data was very positive
Public OLCI/SLSTR L1 data distribution should start after summer followed next year by OLCI/SLSTR L2 data distribution.

## Slide 49: Questions
“Many congratulations to ESA, EUMETSAT, and the European Commission on Sentinel 3A launch & preliminary performance. A new era in ocean colour observations with the first operational ocean constellation - of very high performance sensors! “
(S. Bernard – IOCCG chairman)