## Slide 1: Spectral measurements performed for the development of LIME

## Slide 2: Lunar measurements
Top-of-atmosphere irradiance/reflectance from the ground
Langley plot method in high-altitude stations:
  Izaña (2400m asl)
  Teide (3570m asl)
Two instruments:
  Modified version of Cimel 318T radiometer
  ASD Field Spec
Absolute irradiance
Relative reflectance

## Slide 3: Absolute Irradiance
Cimel 318T – AERONET standard radiometer
Modifications - Bands: 440, 500, 550, 675, 780, 870, 935, 1020, 1640 nm
    Direct Moon polarization measurements
Calibrated at NPL in absolute irradiance responsivity
Full radiometric characterization: reference plane, linearity, temperature dependence, gains, spectral response function.
Data: 2018-2022 (590 clear nights)

## Slide 4: Absolute Irradiance: bands
340
380
440
500
550
675
780
870
936
1020
1640
Si
InGaAs

## Slide 5: Top-of-atmosphere irradiance determination
Direct Moon irradiance observations (8 bands)
Langley plot method + calibration: TOA
Uncertainty

## Slide 6: Moon reflectance
ASD Field Spec 4
Spectral range: 350 – 2500 nm, FWHM 3-16 nm
3 detectors: (350-1000), (1000-1800), (1800-2500 nm)
4 campaigns (April, May, June, September 2022)

## Slide 7: Instrument preparation
Foreoptics
Notes: Christmas wishes
Discussion with VITO >> model requerements and NPL: uncertainty requirements

## Slide 8: Instrument preparation
Optical characterisation at NPL:
  Directional response function
  FOV uniformity (scrambler)
Notes: Christmas wishes
Discussion with VITO >> model requerements and NPL: uncertainty requirements

## Slide 9: Instrument preparation
Enclosure for ASD spectrometer
Temperature control
Notes: Christmas wishes
Discussion with VITO >> model requerements and NPL: uncertainty requirements

## Slide 10: Instrument preparation
Foreoptics for ASD spectrometer: Moon and Sun
ND Filter for SUN measurements
Notes: Christmas wishes
Discussion with VITO >> model requerements and NPL: uncertainty requirements

## Slide 11: ASD data processing
raw>>TOA signals (Sun and Moon)>>reflectance
Phase angles -90º to 90º
60 measurement days, >200k spectra

## Slide 12: Moon spectral reflectance

## Slide 13: Moon spectral reflectance
Normalized to 1240nm

## Slide 14: Moon spectral reflectance
10-deg pase angle bins
Wavelength (nm)
Reflectance

## Slide 15: Summary
Cimel radiometer at high altitude stations Izaña/Teide
  Phase from -90º to +90º
  Since 2018
  TOA irradiance (SI traceable)
  8 narrow bands: 440, 500, 550, 675, 780, 870, 1020, 1640 nm
ASD Fiel Spec
  in 4 lunar cycles (1st to 3rd quarter)
  TOA reflectance (relative)
  350 to 2500 nm (except where absorption by gases)

## Slide 16: Thanks!
Many thanks to the AEMET staff for their support!